## Slide 1
5G PRACH Sniffer — End-to-End Workflow (Overview)
gNB (Laptop 1)
• Configured by .yaml
• Logs interleaved float32 IQ
to .fc32 files
UE (Pixel 6)
• In Faraday box
• Toggle airplane mode → PRACH
preambles
Sniffer (Laptop 2)
• File or USRP mode
• Demodulates PRACH OFDM symbols
• Writes per-worker .fc32 dumps
MATLAB analysis
• Load gNB & sniffer .fc32
• Align SFN/slot/timestamp
• Cross-corr & compute detections
Notes: gNB writes interleaved float32 .fc32; sniffer writes per-worker .fc32 (post-demod, pre-detection).

## Slide 2
Workflow — Detailed Steps & Analysis Checklist
gNB (Laptop 1) — capture
  • Configure YAML to enable phy_rx_symbols: interleaved float32 (.fc32).
  • Record SFN/slot metadata in logs for alignment.
UE (Pixel 6) — stimulus
  • Place in Faraday box; toggle airplane mode to create repeated PRACH attempts.
  • Log time of toggles to help map events.
Sniffer (Laptop 2) — capture & dump
  • Run in file-mode (device_name: "file", rx_channels: [0]) for replay or USRP live.
  • Demodulate PRACH OFDM symbols and write per-worker .fc32 files (post-demod, pre-detect).
  • Use unique filenames: phy_rx_sniffer_worker<id>_sfn<XXXX>_slot<Y>_port<P>_<ts>.fc32
MATLAB analysis — compare & visualize
  • Load .fc32 files → convert to complex IQ (interleaved float32).
  • Align by SFN/slot/timestamp; compensate fractional sample-rate drift.
  • Cross-correlate with PRACH root sequences and compute detections.
  • Measure timing advance differences, missed vs false detections; plot results.